## Slide 1
13 APRIL, 2026
Jorge Garcia Tortosa
Ot Dams
Fernando Sordo
Ulrich Dorda
Mario Perez
BD-OT
Development of the DUMP-OT for MYRRHA phase I accelerator

## Slide 2
Same design concept for both Beam Dumps:
Dump-OT
Energy 17 MeV 100 MeV
Pulse length 4 ms 4 ms
Rep. Rate 10 Hz 2.5 Hz
Duty 4 % 1%
Av. current 4 mA 4 mA
40 mm 40 mm
Power 3.0 kW 4.0 kW
2
SCK-CEN: MYRRHA – Minerva
MYRRHA
Reactor powered by a particle accelerator
  Minerva
  1st phase: first part of overall accelerator – research facility
  Injector 17 MeV
  ADS 100 MeV
I1-DL DUMP
TS-S03 DUMP
Taking advantage of the similar deposited power

## Slide 3
3
BD-OT: Operational Concept
17/100 MeV Proton Beam
17/100 MeV Proton Beam
BD-OT Basic Model (Vessel + Dump material)
Bolt heads: “Mushrooms” (Independent square tiles that accommodate the heat deposited by the beam)
slope
𝛼
The 6° slope increases the effective footprint area by a factor of , effectively reducing the peak power density and distributing the thermal load more efficiently across the dump material.
(perpendicular)
(tilted)
Vacuum vessel
Dump material

## Slide 4
4
BD-OT: Operational Concept
operational concept
22°C water
Contact behaviour
Conservative model
Realistic model
The behaviour of the component thermal mechanism approaches to a realistic model the higher the temperature in the mushrooms
max
24.021 mm
min
24.002 mm
Real Prototype
BD-OT Dump Material

## Slide 5
5
BD-OT: Cooling
A
A’
Welded plug
Drilled channels
Channel characteristics
Cooling parameters
()
Dittus-Boelter
conservative HTC used in the model:
Operational data
Expected water bulk temperature increase:
(negligible impact)
BD-OT Dump Material

## Slide 6
6
BD-OT: Monitoring
Thermocouple sensitive point
Standard feedthrough
Mushrooms have a hole in the centre to accommodate a thermocouple. Number of thermocouples and their position (selected mushrooms to monitor) can be determined per convenience.
  10 thermocouples are introduced through standard feedthrough in the front flange.
  Four – Six central mushrooms are mandatory to monitor (beam impact – per thermal results).
  Thermocouples Type K of chromel(+)/alumel(-) insulated with alumina are a good option for the expected operation temperature range. More expensive Type N may be an option if reliability is a high priority.
  Mineral insulated cables shall be used inside the vacuum vessel.

## Slide 7
7
BD-OT: Conservative Model – Boundary conditions
Convection (water channel)
Heat footprint from MCNP model
  4 (3) kW:
    3.8 (2.85) kW on the dump material
    0.2 (0.15) kW on the vessel (backscattering)
Convection term:
  (From Dittus-Boelter Eq. - Conservative)
Contact modelling:
  Axial contact only – Frictional with
(per analysis)
(conductance)
*Conservative assumption from Yovanovich[1][2]
Energy 17 MeV 100 MeV
Pulse length 1.5 ms 4 ms
Rep. Rate 10 Hz 2.5 Hz
Duty 4 % 1%
Av. current 4 mA 4 mA
40 mm 40 mm
Power 3.0 kW 4.0 kW
I1-DL DUMP
TS-S03 DUMP
Superficial footprint
Bragg peak ≈ 0.75 mm
I1-DL DUMP
(17 MeV)
TS-S03 DUMP (100 MeV)

## Slide 8
8
BD-OT: Conservative Model – Boundary conditions
(conductance)
*Conservative assumption from Yovanovich[1][2]
Water inlet
Water outlet
Welded areas
Heat footprint from MCNP model
  4 (3) kW:
    3.8 (2.85) kW on the dump material
    0.2 (0.15) kW on the vessel (backscattering)
Convection term:
  (From Dittus-Boelter Eq. - Conservative)
Contact modelling:
  Axial contact only – Frictional with
Water inlet
Water outlet
Energy 17 MeV 100 MeV
Pulse length 1.5 ms 4 ms
Rep. Rate 10 Hz 2.5 Hz
Duty 4 % 1%
Av. current 4 mA 4 mA
40 mm 40 mm
Power 3.0 kW 4.0 kW
I1-DL DUMP
TS-S03 DUMP

## Slide 9
MCNP vs Thermal (energy balance check)
9
BD-OT: Conservative Model – Results: 100 MeV
Temperature
(°C)
Steady state
CuCrZr recommended upper temperature limit is 350°C [3].
100 MeV
MCNP
ANSYS
3.3% of pulse time

## Slide 10
3.3% of pulse time
10
BD-OT: Conservative Model – Results: 100 MeV
Eq. Stress
(MPa)
After pulse
Before pulse
195 MPa
Secondary loads are critical for the Beam Dump operational life. Following the work of Heikkinen[4] on CuCrZr, fatigue strength for ultra high cycling is 170 Mpa. Maximum stress range expected is near acceptable limits.

## Slide 11
MCNP vs Thermal (energy balance check)
11
BD-OT: Conservative Model – Results: 17 MeV
Temperature
(°C)
Steady state
CuCrZr recommended upper temperature limit is 350°C [3].
17 MeV
MCNP
ANSYS

## Slide 12
12
BD-OT: Conservative Model – Results: 17 MeV
Eq. Stress
(MPa)
After pulse
Before pulse
148 MPa
Secondary loads are critical for the Beam Dump operational life. Following the work of Heikkinen[4] on CuCrZr, fatigue strength for ultra high cycling is 170 Mpa. Maximum stress range expected remains well below acceptable limits.

## Slide 13
13
BD-OT: Assembly drawings
Assembly drawings already generated before manufacturing phase. Ready to generate accordingly detailed pieces drawings for BD manufacturing phase.

## Slide 14
14
BD-OT: Prototype
Prototype is being manufactured. Cooled block and mushrooms have been machined without issues. Welds with Electron-Beam welding process still to be produced.
mushroom
Cooled Block
Water inlet
Water outlet
Thermocouple hole

## Slide 15
15
Conclusions
A Beam Dump concept has been presented for Minerva Facility for 17 & 100 MeV and 3 – 4 kW beam.
The design solution consists of independent CuCrZr bolts with a planar-squared head called “mushrooms” bolted to a cooled block. The heat transfer mechanism that governs is the contact between the bolt – which receives the beam impact – and the water-cooled block – which evacuates heat through cooling channels– . [The closer the heat transfer between components is to an ideal case (perfect contact → infinite thermal conductance), the more optimal the solution becomes.]
Thermal and mechanical results with a conservative model show good behaviour of the Beam Dumps under nominal conditions (SCK – Accelerator Team beam characteristics):
  For the Injector BD (17 MeV):
    Maximum temperatures below CuCrZr recommended limit (350°C).
    Fatigue is not expected due to secondary loads.
  For the Tuning BD (100 MeV):
    Maximum temperatures below CuCrZr recommended limit (350°C) except during brief beam pulse phases, which account for only 3% of the nominal operation time.
    Fatigue is not expected due to secondary loads.
Prototyping: The concept is already in a prototyping manufacturing phase. Assembly drawings have been produced, and a first prototype is being manufactured (cooled block sample + 6 mushrooms).

## Slide 16
16
References
[1] Cooper, M.G.; Mikic, B.B.; Yovanovich, M.M. (1969), “Thermal Contact Conductance,” International Journal of Heat and Mass Transfer, 12, 279–300.
[2] Yovanovich, M.M. (1982), “Thermal Contact Correlations,” Progress in Astronautics and Aeronautics, Vol. 83, p. 83.
[3] Zhang et al. (2019), “Development of the material property handbook and database of CuCrZr,” Fusion Engineering and Design, 144, 148-153.
[4] S. Heikkinen (2010), “Thermally Induced Ultra High Cycle Fatigue of Copper Alloys of the High Gradient Accelerator Structures,” Aalto University.