## Slide 1: An overview of new developments in McStas
Peter Willendrup, ESS DMSC & DTU Physics
Mads BERTELSEN, ESS DMSC GregorY S. Tucker, ESS DMSC
Damian M. RodrigueS, ESS DMSc
Thomas Kittelmann, ESS DMSC

## Slide 2: Agenda
Brief McStas intro
Presentation of “recent” i.e. 3.0-3.6.x features (not at since 2019) exemplified through
  McStas effort toward ESS commissioning phase
  Securing a improved / solid technical foundation:
    conda-forge, continuous integration, release early/often
  Support infrastructure
    PR-template for user contributions
    Issue-templates
Thanks / funding

## Slide 3: McStas Introduction
Flexible, general simulation utility for neutron scattering experiments.
Original design for Monte carlo Simulation of triple axis spectrometers
Developed at DTU Physics, ILL, PSI, Uni CPH, ESS DMSC
V. 1.0 by K Nielsen & K Lefmann (1998) RISØ
Currently ~6 people on joint McStas-McXtrace team but only 2 full time, based at ESS DMSC / DTU
GNU GPL v3 license
Open Source
mcstas-users@mcstas.org mailinglist
Project website at
http://www.mcstas.org
Peter Kjær Willendrup peter.willendrup@ess.eu
Mads Bertelsen mads.bertelsen@ess.eu

## Slide 4
4
McXtrace - since jan 2009 similar for X-rays
Synergy, knowledge transfer, shared infrastructure, repo etc.
mcxtrace-users@mcxtrace.org mailinglist
Project website at
http://www.mcxtrace.org
Original consortium

## Slide 5: McStas: simulation toolkit for neutron scattering instruments, virtual experiments
Sample-environments - Union subsystem
+
~600
McStas 3.x acc. on NVIDIA GPUs - 1-3 orders of magnitude speedup wrt. single core performance. Talk to Peter for details
Since 2020: McStas 3.x with support for MPI and multiple GPUs
+
Detectors
Neutron optics
Starts with a source of neutrons, be it a reactor- or spallation source
Neutron moderators is where starts
Scientific model-samples

## Slide 6: High McStas fidelity is achieved by interfaces to surrounding community codes, e.g.
Benchmarked material cross-section database
Solutions for elastic and inelastic scattering
Uniform use (cfg strings) across client codes
Monte Carlo Particle List file format
Provides a well-defined interface between many Monte Carlo codes
Widely accepted standard format
GNU Scientific Library (GSL)
Other important libraries
Thomas Kittelmann thomas.kittelmann@ess.eu
See presentation from Thomas Kittelmann right before break!
conda-forge ensures coherence and interoperability

## Slide 7: Reliability - cross comparisons
Much effort has gone into this
Here: simulations vs. exp. at powder diffract. DMC, PSI
The bottom line is
McStas agree very well with other packages (NISP, Vitess, SIMRES, MCViNE)
Experimental line shapes are within 5%
Absolute intensities are within 10%
Common understanding: McStas and similar codes are reliable
P. Willendrup et al., Physica B, 386, (2006), 1032.
E. Farhi, P. Willendrup, from IN22 benchmark exp.
https://doi.org/10.1016/j.nima.2024.169291
Gold foil intensity measurements
KANDI-II 2.47 Å wavelength
Si
Gr2GaC
KARL Si sample
PG 2.421 Å
Cu 0.98 Å

## Slide 8: McStas: simulation toolkit for neutron scattering instruments, V.E.
Work in GUI or fav. editor using DSL or …
… in .py / Jupyter notebooks using McStasscript

## Slide 9
FULL
McStasToX
ESS DMSC Modelling Group “McCode++”
( + .deb Linux packages for most, mccode.org and )
Peter Kjær Willendrup peter.willendrup@ess.eu
Mads Bertelsen mads.bertelsen@ess.eu
Thomas Kittelmann thomas.kittelmann@ess.eu
Damian Martin Rodriguez damian.rodriguez@ess.eu
Gregory Tucker gregory.tucker@ess.eu
( + )
conda-forge also for deployment on and the esss.dk / DMSC cluster

## Slide 10: MC-raytracing instrument modelling is by now standard for instrument design (@ILL, @PSI, @ANSTO, @SAFARI @SNS, @ISIS, @J-PARC, @CSNS, @ESS…)
E.g. at ESS
  All instruments modelled during design phase using McStas + Vitess + SIMRES
  MCNP(x), FLUKA, Geant4 source term, shielding and detectors etc. requiring full energy range and/or non-neutron particle transport
Goal:
Validated, well understood, workable model
Common tool for Modellers, IDS and instrument team
One main source
  Branch off to do specific tasks
Status of ESS McStas models: Transitioning to commissioning
Setting up dedicated repos at ESS DMSC
  Simplification (parameters varied during design should become “frozen” etc.)
  Aiming for similar
    Look and feel
    Naming of components and variables, concepts
  DMSC “modelling” group in close collaboration with IDS group
Commissioning….

## Slide 11: How will the source perform during ramp-up?
The model available in McStas corresponds to the “asymptotic expected behaviour” of the butterfly source
Anything beyond that will require work from the target group. I have proposed they create MCPL input files corresponding to “logical steps” during ramp-up of proton energy and accelerator power
Until such a suite of input files exist, your guess is as good as mine ;-)
In the meantime, one might try using
  (Iill not change spectrum shape - and time-profiles remain the same…)
Use the “generic pulsed source” contributed by Klaus Lieutenant
Keep an eye open for incoming developments in collab. with ESS Spallation Physics Group

## Slide 12: CAD / geometry validation help - 1
Import CAD data into McStas:
  Use e.g. Shape.comp in McStas, import CAD from the engineer
  Check that McStas model and what was ordered / built agrees
  Caveat: We support OFF format only ;-)
  A possible route:
  Catia/Solidworks/etc -> STL -> OFF via FreeCAD
BIFROST guide assembly from CAD (CYAN) imported alongside McStas guide elements
ILL cryo-furnace in mcdisplay

## Slide 13: CAD / geometry validation help - 2
Import McStas visualisation data into CAD
mcdisplay-cad from Greg Tucker depends on CadQuery* / OpenCASCADE and exports many different formats - Choose between STEP, STL, VRML, GLTF, VTKJS, and OpenCASCADE Technology XML
Comp geometry data only - rays are ignored
Should work with the engineer’s favourite geometry tool!
* to use with a standard McStas install, please inject cadquery via e.g. micromamba install cadquery
Here used to visualise sample-detector path on BIFROST - model from Milan Klausz
Gregory Tucker gregory.tucker@ess.eu

## Slide 14: “Richer NeXus format”
All component AT / ROTATED data
All component param=value info (currently as text from instr file)
Monitor_nD geometry data included
Monitor_nD binning / pixellation arrays

## Slide 15: Easier access to data interpretation - 1
McStas to McStasScript / Jupyter

## Slide 16: Easier access to data interpretation - 2
Via NeXus to nexpy
Enables easy access to fitting etc.

## Slide 17: New stuff in the series 3.5.x and 3.6.x
Common release and versioning for McStas & McXtrace - no more 2.x and 1.x
We are now on conda-forge!
  Forms support basis for Windows, macOS and non-Debian Linux
Lots of work from SOLEIL toward official Debian packages
CI (GitHub + conda) in place
Usability:
  One-click transfer to McStasScript/Jupyter
  Easy access to NeXus output through e.g. nexpy or silx
  3D rendering modernised
mctest / mcviewtest tools
Various component / instr contributions
LOTS of work on many layers + infrastructure -> solid basis for future work:
  Used for preparing the ESS data pipeline
  More emphasis on “in-experiment” and data-analysis features
  Further modernisation
Project:
  Historical “yearly release” -> release often, release early mode(conda-forge is the basis)
  PR-only, “production grade” main branch
  Plan to extend McStas/McXtrace collaboration
  Even more emphasis on testing at different levels

## Slide 18: New stuff in the series 3.5.x and 3.6.x
Common release and versioning for McStas & McXtrace - no more 2.x and 1.x
We are now on conda-forge!
  Forms support basis for Windows, macOS and non-Debian Linux
Lots of work from SOLEIL toward official Debian packages
CI (GitHub + conda) in place
Usability:
  One-click transfer to McStasScript/Jupyter
  Easy access to NeXus output through e.g. nexpy or silx
  3D rendering modernised
mctest / mcviewtest tools
Various component / instr contributions, some presented later today!
(base) laptop:~ user$ mctest --instr=BNL_H8 -n1e7 --testdir=$PWD --mpi=10
loading system configuration
Output of test will be placed in: /Users/user
ncount is: 1e7
mpi count is: 10
Testing: 3.6.13
Finding instruments in: /Users/user/micromamba/share/mcstas/resources/examples
Copying instruments to: /Users/user/mcstas-3.6.13_mpi_x_10_BNL_H8_Darwin
Compiling instruments [seconds]...
BNL_H8 : 6.52
BNL_H8_simple : 2.34
Running tests / getting status...
BNL_H8 : 5.08 [val: 9.60477e-10 / 9.84026e-10 = 98 %]
BNL_H8_simple : 2.13 [val: 9.53534e-10 / 9.84026e-10 = 97 %]
======================================
Overall test result:
SUCCESS
New, ~ “feature-complete” python/ANTLR4 code-generator mcstas-antlr from G S Tucker. install from e.g. conda-forge Want to know more? Talk to Greg

## Slide 19: Better Quality Assurance of incoming McStas contributions
ICANS XXV 2026 Malmö
Have in essence handled much this task in alone since 2002
PW dealt with almost all user-support in the past 24 years (Lots of mcstas-users posts, personal emails, GitHub issues, …)
Experience: very few “component-developers” stay in the game
Very few “component-developers” touch (the distributed version of) their code ever again
What to do going forward?
Insist contributor is part of the process via GitHub PR as long as possible. (Also: code can no longer be sent via email etc.)
Raise the bar for acceptance a bit (Includes checklist / reminders of what to do)
Teach use of relevant development tools and apply Continuous Integration (CI) tests
- This means that PR/merge time is effectively my LAST chance
This will of course NOT mean that I / the other McCode dev’s will leave everything to you! Your PR and the repo are meant for collaboration!

## Slide 20: Interface physics demo
PRESENTATION TITLE/FOOTER
2025-07-10
McStas
Lots of other news… New components, new capabilities, new physics has also come in… Example: Interface physics in McStas union assemblies. Talk to Mads for details!
Mads Bertelsen mads.bertelsen@ess.eu

## Slide 21: Conclusion
McStas is in great shape!
Lots of work on basic infrastructure, development tools, CI, packaging
Lots of new features e.g. for use in ESS commissioning
Please make good use of GitHub infrastructure (PRs and issues)
Peter Kjær Willendrup peter.willendrup@ess.eu
Mads Bertelsen mads.bertelsen@ess.eu
Thomas Kittelmann thomas.kittelmann@ess.eu
Damian Martin Rodriguez damian.rodriguez@ess.eu
Gregory Tucker gregory.tucker@ess.eu
( + )
ICANS XXV 2026 Malmö
McStas/McXtrace/AI summerschool in September, check mcstas.org website:
lightning talks during ICANS Tuesday poster session: | 
Nicolò Violini | Artificial Intelligence applied to Neutron simulations
Nicola Rizzi | Thick 3He detector component for time-of-flight energy resolution calculation
Gregory tucker | The case for mccode-antlr
Shuqi Xu | Quantitative data analysis of neutron imaging experiments using NCrystal
Gabriele Sala | 1) McStas to Mantid conversion, generation of the IDF and Nexus file. 2) Request for an update of Union_mesh component 3) Request to add on the McStas website a tab to upload sample environment templates
Peter Willendrup | A quick look at the PR template / contribution process
Thomas Kittelmann | Overview of MCPL + NCrystal in McStas
Mads Bertelsen | Union interface physics
You? | Bring maximum 1 slide - or just a theme for discussion!

## Slide 22: Backup Slides

## Slide 23: Main McStas Funding sources

## Slide 24: What constitutes a high-quality component contribution?
A piece of code that serves a well-defined purpose, generalised as far as possible
Comes with a(t least one) test (%Example pars=value Detector: what_I=to_expect)
Uses the standard physical units and parameter names of McStas (NOMENCLATURE)
Has the right type of code in the right %{ %} sections
Has sufficient, meaningful and complete documentation
Can be read and understood by others (and yourself later, weeks-months is enough to loose track) (Prefer simplicity over complexity in algorithms, doc strings etc. Think of your peer user.)
Is aligned with / flavoured and styled like other similar components (Please dig in comp and instr database, much to inspire from!)
Runs across platforms (ideally including on GPU)
Includes vetted / linted c-code and does not spit out lots of noise
conda-forge and GitHub CI helps!
Much of this is documented on the Wiki and you are reminded during the PR process