## Slide 1: New Front-End Design Requirements for LANSCE Neutron Sources: LAMP’s Role in Sustaining High-Quality Beam to the Lujan 1L Target
Charles Taylor, representing the LAMP and LANE collaborations at the LANSCE facility
April 13st, 2026

## Slide 2
LANSCE Overview
The Los Alamos Neutron Science Center (LANSCE) accelerator facility has supported nation-wide science and technology programs for 50+ years
Historically delivers 800-MeV proton beams to six facilities simultaneously
Three major Department of Energy (DOE) Stakeholders:
  Defense Programs (DP)
  DOE Office of Science
  Office of Nuclear Energy, Science and Technology (NE)
Studies at LANSCE include:
  Nuclear weapons program
  National security research
  Radioisotope production
  Basic science- (neutrino & dark matter searches)

## Slide 3
LANSCE overview and missions
~half-mile-long accelerator
Proton Radiography (NA-11, -12, -82)
Proton Storage Ring
H+, H- injectors (750 kV)
201.25-MHz Drift tube linac (to 100 MeV)
Ultracold Neutrons (DOE-SC-NP)
Weapons Neutron Research (NA-11, -12, -82, -ESH, global
security, industry)
Lujan Center (NA-11, -19, -82, -ESH, DOE-NE, -SC-HEP)
805-MHz Side-coupled linac (100-800 MeV)
Area A
Isotope Production (SC-IRDP, NA-11, -22, -ESH)

## Slide 4
LANSCE has Unique Beam Capabilities for User Facilities
LANSCE’s uniqueness is not just beam power—it is the ability to deliver multiple, highly specialized beam formats at the same time.
Simultaneous beam delivery to multiple user facilities
Dynamic beam sharing within a single accelerator cycle of 120 Hz operation
Dual-species operation (H⁺ and H⁻) with independent optimization
Flexible time structures: µs macropulses to ns bunches
Facility-specific beam tailoring (Lujan, WNR, pRad, IPF, UCN) Proton Storage Ring compresses pulses to 100–300 ns
Enables high-resolution neutron and radiography experiments
High flexibility comes with strong sensitivity to front-end performance

## Slide 5
LANSCE Operational Challenges
Revision 0 of the Run Cycle
Aging accelerator infrastructure
RF and klystron system failures
High Voltage Power Supply (HVPS) instability
Frequent beam trips and interruptions
Cooling water system leaks and inefficiencies
Vacuum system degradation
Run cycle inefficiencies
Obsolete components and spare parts shortages
Increasing operational risk
Reduced beam availability for users

## Slide 6
LANSCE Upgrade Projects
LANSCE Upgrades
LAMP: Modernizing the Foundation
  Replaces aging front-end accelerator systems
  Improves reliability and beam availability
  Reduces single-point failures
  Ensures operations through ~2050
  Focused on sustaining existing mission capabilities
LAMP keeps LANSCE running for decades to come
LANE: Expanding the Mission Space
  LANSCE Enhancements (LANE) initiative
  Focused on advancing experimental capabilities
  Driven by evolving NNSA mission needs
  Potential expansion of:
    Proton Radiography
    Neutron science
    Advanced materials diagnostics
    Area A restoration
  Positions LANSCE for next-generation national security challenges
LANE keeps LANSCE running for decades to come

## Slide 7: The project mandate is to keep the present machine capabilities with a modernized and more reliable front end
Radio Frequency Quadrupole (RFQ) 100 keV  3 MeV
Modern drift tube linac (SNS @ ORNL)
H+
Existing Cockcroft-Waltons
35 keV  750 keV
2 x (10 m x 15 m x 10 m)
H-
SNS H- ion source
High reliability and uptime
High beam current
~ 250 mm Φ
LANSCE Modernization Project (LAMP)

## Slide 8
LAMP Project Scope
Design & Technology Development
Front-end physics and engineering design spanning ion sources, LEBT, RFQ, MEBT, and DTL systems
Integration modeling to ensure beam delivery requirements are met for all user facilities (Lujan, WNR, UCN, IPF)
Technology maturation of critical systems including RFQ test stands, beam choppers, and diagnostics
Decommissioning (D&D) & Facility Preparation
Removal of legacy Cockcroft-Walton injectors and aging drift tube linac component
Digitization of the existing facility via large-scale point-cloud scanning to support removal and redesign
Conversion of scanned geometry into CAD models for installation planning and interference checks
Infrastructure preparation including integration with existing utilities, shielding, and facility constraints
Construction, Installation & Commissioning
Fabrication and installation of new RFQ-based injector and modern DTL systems
Integration of accelerator subsystems (RF, controls, diagnostics, vacuum, power)
Pre-installation verification testing and staged system validation prior to beam operations
Beam commissioning and ramp-up to meet operational requirements while maintaining existing mission capabilities

## Slide 9
Preliminary Simulations of the LAMP Components
Simulation work presented in DOI:https://doi.org/10.2172/2315684 [LA-UR-24-21709]
Model of low-frequency buncher for LAMP (16.67 MHz), re-designed for 100keV H- beam, [J. Upadhyay]
A transverse cut showcasing the model of the H+ source in Warp [S.I. Sosa Guitron]
Transverse dynamics in the MEBT with H- beam [S.I. Sosa Guitron]
shows the longitudinal rms size as the initial beam is compressed with the LFB at z= 4.2 meters for MPEG-like beam [S.I. Sosa Guitron]
The handshake between the RFQ and MEBT simulations. At the top, H+ beam at the end of the RFQ as calculated by Parmteq, at the bottom, the input beam read by Impact-T for the MEBT simulation. The RFQ was designed to output the same phase space distribution for both H+ and H- beams into the MEBT. This way, the MEBT can transport both species of beams

## Slide 10: Published Point Cloud – 500 Scan Locations
Digitization of Existing Facility
Measurement of the facility and it sub-systems has been digitized
New point-cloud models are being used for D&D and upgrade model designs

## Slide 11: Published Point Cloud – LANSCE Front End
From LA-UR-25-31512
Nearly the entire facility has been scanned
Conversion to CAD models is underway

## Slide 12: Recreated Beam Areas

## Slide 13: Lujan Requirement
AP.25: Lujan1 (LBEG/PSR) Mpulse freq: 20 Hz |  | 100 µA at end station #µp/Mp: 102k |  | 
location | charge | cur(5ns) | assumed trans. | 
1L target | 49 pC | 9.8 mA | foil->end | 0.95
PSR.foil | 52 pC | 10.3 mA | TR->foil | 0.98
TR.entrance | 53 pC | 10.5 mA | DTL | 0.80
DTL.entrance | 66 pC | 13.2 mA | MEBT | 0.97
 |  |  | RFQ | 
MEBT.entrance | 68 pC | 13.6 mA | [Q/Q] | 0.95
 |  |  | LFB | 
RFQ.entrance | 72 pC | 14.3 mA | bonus | 1.00
LFB.entrance | 72 pC | 14.3 mA | LEBT | 0.98
H– source | 73 pC | 14.6 mA |  | 
*transmission assumptions based on experimental measurements or simulations
LAMP design shall provide a H- beam at the Lujan Center 1L target with the following characteristics: 100 µA average beam current, structured as 120-nsec (FWHM) pulses at 20 Hz.
Energy Resolved Neutron Imaging (ERNI)
Asterix
High-Pressure-Preferred Orientation (HIPPO)
Spectrometer for Materials Research at Temperature and Stress (SMARTS)

## Slide 14
AP.35: WNR1 (MPEG) Mpulse freq: 100 Hz |  | 4 µA at end station #µp/Mp: 347 |  | 
location | charge | cur(5ns) | assumed trans. | 
Target 4 | 115 pC | 23.0 mA | TR->end | 0.90
TR.entrance | 128 pC | 25.6 mA | DTL | 0.80
DTL.entrance | 160 pC | 32.0 mA | MEBT | 0.90
 |  |  | RFQ | 
MEBT.entrance | 178 pC | 35.6 mA | [Q/Q] | 0.70
 |  |  | LFB | 
RFQ.entrance | 254 pC | 50.8 mA | bonus | 1.70
LFB.entrance | 149 pC | 29.9 mA | LEBT | 0.98
H– source | 152 pC | 30.5 mA |  | 
WNR Requirement
LAMP design shall provide a H- beam at the WNR target 4 with the following characteristics: 4 µA average beam current, structured as 625-µsec (FWHM) trains of individual pulses separated by 1.8 µsec.
Detector for Advanced Neutron Capture Experiments (DANCE)
Device for Indirect Capture Experiments on Radionuclides (DICER)

## Slide 15
AP.50: UCN #Mpulse/5sec: | 10 | 10 µA at end station #µp/Mp 126k |  | 
location | charge | cur(5ns) | assumed trans. | 
Target | 40 pC | 8.0 mA | TR->end | 0.97
TR.entrance | 41 pC | 8.2 mA | DTL | 0.80
DTL.entrance | 51 pC | 10.2 mA | MEBT | 0.97
 |  |  | RFQ | 
MEBT.entrance | 53 pC | 10.6 mA | [Q/Q] | 0.95
 |  |  | LFB | 
RFQ.entrance | 56 pC | 11.1 mA | bonus | 1.00
LFB.entrance | 56 pC | 11.1 mA | LEBT | 0.98
H– source | 57 pC | 11.3 mA |  | 
UCN Requirement
LAMP design shall provide a H- beam to LANSCE line B, UCN facility, with the following characteristics: 10 µA average beam current, nominally 9–11 pulses of 625-µsec width, at 20 Hz every 5 seconds.

## Slide 16
AP.60: IPF Mpulse freq: | 100 Hz | 250 µA at end station #µp/Mp: |  | 102k
location | charge | cur(5ns) | assumed trans. | 
end station | 25 pC | 4.9 mA | TR->end | 0.95
TR.entrance | 25 pC | 5.2 mA | DTL | 0.97
DTL.entrance | 26 pC | 5.3 mA | MEBT | 0.97
MEBT.entrance | 27 pC | 5.5 mA | RFQ [Q/Q] | 0.95
RFQ.entrance | 29 pC | 5.8 mA | LFB bonus | 1.00
LFB.entrance | 29 pC | 5.8 mA | LEBT | 0.98
H– source | 29 pC | 5.9 mA |  | 
LAMP design shall provide a H+ beam to IPF (Isotope Production Facility), with the following characteristics: 250 µA average beam current, structured as 625-µsec pulses.
H+ is its own source, and consistently lower emittance than H–. We adopted LBEG transport for much of H+ design work.
IPF Requirement

## Slide 17
LANE proposes to update LANSCE capability to enhance alignment with NNSA future directions
17
  100-800 MeV proton energies
  Six target stations (three neutron spallation targets)
  Sixteen beam lines (including future capability expansion in Area A)
NNSA work
Key program drivers
LANSCE
LINAC = “Linear Accelerator”
Proton Radiography (pRad Facility)
Dynamic imaging providing focused weapons physics data for models & simulations
Lujan Neutron Scattering Center (Lujan Center)
Materials characterization supporting aging, manufacturing, and performance as well as nuclear energy
Nuclear physics for defense programs
Weapons Neutron Research Facility (WNR)
Nuclear physics serving weapons assessments, counterproliferation, and criticality safety
Electronics testing for industry and global security
Isotope Production Facility (IPF)
Medical and other isotopes for the isotope program
Short-lived isotopes for defense programs, non-/counterproliferation, and criticality safety
Ultra-Cold Neutron Facility (UCN)
Unique probe for nuclear physics, possible future defense program uses
LANSCE Upgrades

## Slide 18
LANE Project Scope
Dynamic Imaging
Multi-pulse x-ray source for pRad
Additional proton radiography beamline in LANSCE Area A
Additional drivers and diagnostics
pRad energy upgrade
Materials Characterization
Dedicated beam line for classified experiments
New multi-probe flight path for imaging and bulk characterization
Compact x-ray source for small scale, hazardous, classified experiments.
Materials Characterization
Expanded WNR capabilities for radioactive targets
Partnering with Isotope Production Facility for improved targetry
A neutron target facility to measure short-lived isotopes

## Slide 19
LANE would add NNSA mission driven capabilities
LANSCE Upgrades

## Slide 20
LANE uses a phased approach to implement upgrades
LANSCE Upgrades
Potential enhancements in current LANE concept

## Slide 21
Line A Modernization paves the way for LANE activities
LANSCE Upgrades

## Slide 22
Summary
LAMP Objective Requirements are to achieve the desired operational conditions
Replaces aging front-end systems to reduce failures, downtime, and operational risk
Establishes a modern RFQ-based injector and upgraded DTL for improved beam quality and stability
Eliminates single-point failures and addresses obsolescence in critical infrastructure
Enables consistent delivery of complex beam structures required by Lujan, WNR, UCN, IPF, and pRad
Supports ~5,300 annual beam hours with improved reliability and maintainability
Preserves current mission capabilities while extending operational lifetime through ~2050Provides a stable foundation for future upgrades and integration with LANE enhancements
LANE Objectives are Currently be Scoped this Fiscal Year
Expands LANSCE experimental capabilities by enabling next-generation beamlines, diagnostics, and user facilities aligned with evolving NNSA mission needs
Positions LANSCE for future mission growth through enhanced performance, flexibility, and restoration/expansion of experimental areas such as Area A

## Slide 23
Questions?

## Slide 24
Backup Slides

## Slide 25
The LANSCE Complex
N
Chopper
Kicker
201.25-MHz 100-MeV Drift Tube Linac
Transition Region
H+
H-
750-keV Cockcroft-Walton Injectors
Isotope Production Facility
Proton Radiography
80—MHz 800-MeV Coupled Cavity Linac
Ultra-Cold Neutrons
Area A
(currently inactive)
Lujan Center
Proton Storage Ring
Target 4
Target 2
Target 1
ER-1
Isotope Production Facility (IPF)
  High-current (100 MeV H⁺) beam for medical and national security isotope production
  Emphasis on reliability and sustained beam current
Proton Radiography (pRad)
  High-energy proton imaging for dynamic experiments (e.g., hydrodynamics)
  Requires precisely structured burst-mode beam delivery
Ultra-Cold Neutron (UCN) Facility
  Fundamental physics experiments using moderated neutron beams
  Requires specialized low-duty-factor beam delivery
Lujan Neutron Scattering Center (1L target focus)
  Pulsed spallation neutron source for materials science, nuclear energy, and weapons-relevant studies
  Requires high-quality, well-defined pulse structure and stable beam delivery
Weapons Neutron Research (WNR)
  Operates with micropulse structures (µs spacing) and flexible timing modes
  Broad-spectrum neutron source for nuclear data, cross sections, and radiation effects
A. L. Cooper et al., High-intensity, low-energy heavy ion source for a neutron target proof-of-principle experiment at LANSCE, LA-UR-23-31433 (2024).