## Slide 1
Tianjiao Liang
China Spallation Neutron Source (CSNS)
Institute of High Energy Physics， Chinese Academy of Sciences
ICANS XXV meeting, Malmö, Sweden, Apr. 13, 2026
Status of CSNS Neutron Instruments

## Slide 2
Outline
CSNS Instrument Suite
Powder & single crystal diffractometers
Large scale instruments
Inelastic spectrometers
Industry application and nuclear technique
Summary

## Slide 3
3
China Spallation Neutron Source
CSNS-I (2011-2018)：Accelerator and target station 100kW, 3 instruments.
CSNS-CI (2018-2025)：8 instruments，trial or open to user.
CSNS-II (2024-2029)：Accelerator and target station 500kW, 11 instruments & station.
Layout of CSNS-I

## Slide 4
Powder Diffractometer | General Purpose Powder Diffractometer (GPPD)
 | Multi Physics Instrument (MPI)
 | High-resolution Powder Diffractometer (TREND)
 | High pressure diffractometer (HP)
Large Scale | Small Angle Neutron Scattering instrument (SANS)
 | Very Small Angle Neutron Scattering (VSANS)
 | Multi-Purpose Reflectometer (MR)
 | Liquid Neutron Reflectometer (LNR)
Industry Application | Engineering Material Diffractometer (EMD)
 | Energy Resolved Neutron Imaging (ERNI)
 | Atmosphere Neutron Irradiation (ANIS)
Direct Geometry Spectrometer | High energy inelastic spectrometer (HD)
 | Cold Neutron Inelastic Spectrometer (CNIS)
 | Polarized Neutron Spectrometer (PAINTER)
Indirect Geometry Spectrometer | Molecular Vibration Spectrometer (iMovies)
 | Neutron Backscattering Spectrometer (NuBS)
Single Crystal | Elastic Diffuse Scattering Spectrometer (EDS)
 | Single Crystal Neutron Diffractometer (SCND)
Nuclear physics & technique | Back-streaming white neutrons (Back-n)
 | Neutron Technology Develop Station (NTDS)
 | Neutron Physics & Application Instrument (NPAI)
 | High-energy Proton Experimental Station（HPES）
 | Muon station（MELODY）
CSNS Instrument Suite
4
CSNS-I CSNS-CI CSNS-II
Couple Hydrogen Mod. BL01-04
DPHM. BL18-20
Couple Hydrogen Mod. BL12-14
DPHM. BL8-10
DWM. BL05-07
DWM. BL15-17

## Slide 5: Operating Instruments
Powder Diffractometer | GPPD
 | MPI
 | HRD
 | HPND
Large scale | SANS
 | MR
 | VSANS
Industry application | EMD
 | ERNI
 | ANIS
Inelastic | HD
2017 |  |  |  | 2018 |  |  |  | 2019 |  |  |  | 2020 |  |  |  | 2021 |  |  |  | 2022 |  |  |  | 2023 |  |  |  | 2024 |  |  |  | 2025 |  |  |  | 2026 |  |  | 
3 | 6 | 9 | 12 | 3 | 6 | 9 | 12 | 3 | 6 | 9 | 12 | 3 | 6 | 9 | 12 | 3 | 6 | 9 | 12 | 3 | 6 | 9 | 12 | 3 | 6 | 9 | 12 | 3 | 6 | 9 | 12 | 3 | 6 | 9 | 12 | 3 | 6 | 9 | 12
2018.9
2017.11
Commissioning
Open to user
2017.11
Commissioning
Open to user
2017.11
Commissioning
Open to user
2018.9
Open to user
Commissioning
2021.7
2021.11
Construction & Installation
Design
2018.7
Design
2020.7
2023.1
Commissioning
2024.3
Open to user
Design
2021.7
2024.7
Commissioning
2020.1
2020.7
Design
Commissioning
2018.5
2024.7
2018.7
Design
2020.7
2023.1
Commissioning
2024.3
Open to user
Commissioning
2017.9
2020.7
2022.4
2022.10
Design
Trial operation
2019.7
2020.7
Design
2023.1
2024.10
Trial operation
Commissioning
2022.12
Commissioning
2023.10
Trial operation
2018.5
2020.7
Design
2025.2
Trial operation
Trial operation
2025.2
5
Construction & Installation
Construction & Installation
Construction & Installation
Construction & Installation
Construction & Installation
Construction & Installation
Construction & Installation
Open to user
Open to user

## Slide 6: Schedule of CSNS II Instrument
6

## Slide 7
Outline
CSNS Instrument Suite
Powder & single crystal diffractometers
Large scale instruments
Inelastic spectrometers
Industry application and nuclear technique
Summary

## Slide 8: Overview of Powder Diffractometer
Phase I: Mar 2018
Coorperation: Oct 2021
Coorperation: Jul 2024
Coorperation: Jul 2024
8

## Slide 9
9
Resolution
Flux
0.006
0.0003
0.0015
0.004
1x106
5x107
1x107
4x107
GPPD
TREND
HPND
MPI
Overview of Powder Diffractometer

## Slide 10
Lanthanide all solid-state electrolyte material
Science 368 (2020) 1347–1352 Science 373(2021) 315–320 Nature 614 (2023) 95-101 Nature 616 (2023) 77-83
Science 385 (2024) 422–427 Science 385(2024) 744–752 Nature 628 (2024) 99-103 Nature 640 (2025) 941-946
10
Scientific Highlight
Ultrastrong Steel
Iron-containing Mordenite
Long-range ordered porous carbon crystal
Enhancement of Plasticity in Ceramics
Air Sensitivity of Na-layered Oxides
Zeolites with Extra-large Pores
Negative thermal expansion and
oxygen-redox electrochemistry

## Slide 11
11
High-Resolution Diffractometer (TREND, BL09)
Detecting tiny structural distortion or critical behavior in condensed matter physics
Determination of complex crystal/magnetic structures of functional materials
In-situ measurements for energy materials in material science
Best resolution: <0.05%
d-range:0.1-25Å@6.25 Hz
Resolution@TREND
Resolution@SuperHRPD
J. Phys. Soc. Jpn. 80 (2011) SB020
NIST Si
Empty
Background@TREND
Background@SuperHRPD
KENS_REPORT XX, P185 (2021)
The background level is about one order of magnitude lower than SuperHRPD.

## Slide 12
12
High Pressure Neutron Diffractometer (HPND)
Hutch 1
Hutch 2
Hutch 1
Hutch 2
Two hutches for different HP devices, the second in-situ neutron diffraction cubic press in the world.
Combining diffraction and imaging to analyze the relationship between structure and properties.
The PE cell can achieve a pressure of 15.5 GPa.

## Slide 13
13
Elastic Diffuse Scattering Spectrometer (BL17)
Study the complex disorder and short-range correlation of spins, vacancies and atomic displacement in single-crystal sample.
Correlation chopper Tcc:Seperation of elastic and inelastic scattering signal.
Frustrated magnets, Quantum magnets, Critical phenomena, Superconductivity, Mulitferric, Ionic conductor, Molecular , Quasi-crystallography
Polarized Neutron option:Seperation of nuclear, magnetic and spin-incoherent scattering.
Dr. Erxi Feng
Decoupled water moderator (DWM)
Flight length: L1 = 22 m；L2 = 2.2 m
Wavelength: 0.5~6.5 Å,
1.5~4.5 Å (polarized)
Detector: He3 PSD
Coverage: -35˚ ~ +145˚ (horizental)
-30˚ ~ +30˚ (vertical)
Q-range: 0.25 ~ 18 Å-1
Q-resolution: < 1.0%

## Slide 14
14
Elastic Diffuse Scattering Spectrometer (BL17)
Expected Performance（Mcstas simulation of Ho2Ti2O7）
EDS 1.5~4.5 Å Flux ~ 1×107 n/cm2/s Qmax ~ 7.5 Å-1
EDS 0.5~6.5 Å Flux ~ 3×107 n/cm2/s Qmax ~ 23.5 Å-1
D7 (polarized)
Flux ~ 2×106 n/cm2/s
Qmax ~ 2.6 Å-1
Science 326 415 (2009)
Large Q coverage enables magnetic and nuclear diffuse scattering observation simultaneously
Magnetic Diffuse（Spin Ice）
Fine Q-resolution allows nuclear and magnetic structure analysis under extreme conditions.
Single-crystal diffraction（HK0）
2023
2024
2025
2026
2027
2028
2029
20??
CSNS-II
Instrument lifecycle
Sep. 2024:
Physical design completed
July. 2025:
Installation
Mid. 2028:
Commissioning & Operation
n

## Slide 15
High-resolution single-crystal diffractometer using wavelength-resolved Laue techniques to address crystallographic and magnetic structural problems in solid-state physics, chemistry, biology materials science, engineering, etc.
Crystallography
Magnetic Structure
Phase Transition
Isotope
H-Atom and H-Bond
Protein
15
Single Crystal Neutron Diffractometer (BL19)
Dr. Sihao Deng
Features
1. High-resolution: d-resolution (∆d/d) < 0.3 %
2. Dual-Mode Optics: HR/HF switch
3. SiPM Detector: Spatial resolution 1 mm，
Best coverage (under evaluation) ~5.55 Ster. (~ 44%)
4. Polarized & Multi-Fields:³He sys, ≥7T, 0.1-2000K
5. Intelligent Beamline: Auto-align & online process
6. Accommodating medium-sized biomolecules up to 100Å cell

## Slide 16
Outline
CSNS Instrument Suite
Powder & single crystal diffractometers
Large scale instruments
Inelastic spectrometers
Industry application and nuclear technique
Summary

## Slide 17
17
Large-Scale Instruments of CSNS
2018-01 commissioning of SANS & MR
2023~2024 Upgrade and commissioning of SANS（120kW）
2023-03 Fully commissioning of VSANS (100kW)
2024-10 Start design of LNR
2028-5 commissioning
（300kW）
2024-03 users program
BL01-Small angle neutron scattering (18m)
BL14-Very small-angle neutron scattering (35m)
BL03- Liquid reflectometer (horizontal)
BL02-Multi-purpose reflectometer（vertical）
Sponsored by Cantonese Government
2018-09
users program
（under construction）

## Slide 18
18
Small-Angle Neutron Scattering
Instruments | SANS-18m（BL-01） |  | VSANS-35m（BL-14）
 | Before 2023 | 2024 - now | 
Moderator | CHM (20K) |  | CHM (20K)
Detector resolution | 8*8.5mm (3He PSD) | 5*8.5mm (3He PSD) | 3 ~1㎡ He-3 PSD 8mm resolution 1210×210 mm2 GEM PSD 2 mm resolution
Wavelength range | 1-10.9 Å | 1 - 12 Å | 2.2－6.7 Å； 6－10.5 Å
Q-range | 0.005 Å-1 - 1Å-1 （SDD：2~4m） | 0.003 Å-1 - 1.77 Å-1 （SDD：2.2~5.2m） | SANS: 0.0016 － 1.8 Å-1 VSANS: 0.00028-0.008 Å-1
Q-resolution | 3.5% @ 0.1 Å-1 | 2.8% @ 0.1 Å-1 | 2.1% @ 0.1 Å-1 for SDD=12.75m
flux @sample pos | 5*106 n/cm2/s@100kW | ~7*106 n/cm2/s@ 170kW | @2.49m, 2.6×107 ； @5.15 m, 9.0×106 @12.75m, 1.6×106； VSANS, 1.3×105
Beam-size @sample pos | 6mm（default），4mm | 8mm（default） 6mm，4mm | SANS: 6, 8, and 15 mm; VSANS: 15×30 mm2
VSANS
SANS
18

## Slide 19
19
Temp control devices
Cryostat
(6~500K)
Furnace
(RT~1200℃)
40 positions sample changer
Stress-temp
Laser emission
Magnetic devices
Hmax：1.7T
Temp：RT
Hmax：3 T
Temp：2-700K
In-situ electrical field
Rheo-SANS
load: 10 kN
Temp: -90~400℃
RT~1000℃
Simultaneous DSC
Temp:-150~500℃
Sample environments of SANS & VSANS
Voltage: 2.5kV
Temperature: RT~100 °C

## Slide 20
20
Magnetic nano-surface/interface (vertical)
NR
Multi-Purpose Reflectometer (BL02)
Adv. Mater. 37, 2413700 (2025)
Magnetic Antiskyrmions possess alternating Bloch- and Néel-type spin spirals
Net Magnetization in AFM
Nature Comm. 15, 4734 ( 2024)

## Slide 21: Liquid Neutron Reflectometer (BL03)
Applications
behaviors of biological membranes proteins at interface
stability of colloidal systems and ions / molecules transport between two liquid phases
electrochemical/chemical reaction at liquid-liquid interfaces
reactions at Liquid-Solid Interfaces During Friction and Corrosion
Parameters | Design value
Moderator | CHM
Wavelength Range | 1~12 Å
Q-range | 0.003~0.6 Å-1
Minimum reflectivity | ~10-6
Resolution（ΔQ/Q） | 2%~10 %
Flux @ Sample | 5×107 (n/cm2/s)
Sample geometry | Horizontal
Experimental Modes | reflection+ GISANS
Detector Efficiency | ≥ 70 % @ 6 Å
Detector resolution | 2mm*2mm
characteristics and innovations
Rapid switching between reflection and GI-SANS experimental modes enabling the 3D interfacial structure measurement
Prof. Yubin Ke
21

## Slide 22
Outline
CSNS Instrument Suite
Powder & single crystal diffractometers
Large scale instruments
Inelastic spectrometers
Industry application and nuclear technique
Summary

## Slide 23: Scientific Goals of Spectrometers
HD
PAINTER
CNIS
Medium-High Ei
Medium-Low Ei
Low Ei
Medium E-Resolution
Medium E-Resolution
High E-Resolution
Physics:
  lattice dynamics,
  spin dynamics,
  molecular vibrations,
  ion diffusion/reorientation,
  nuclear spin excitation, etc.
  Materials:
  magnetic materials,
  high-temperature superconductors,
  energy materials,
  Catalyst
  life science materials, etc.
Polarization Analysis
iMovies
Medium Ei
High E-Resolution
NuBS
Low Ei
High E-Resolution
23

## Slide 24
24
Name | Parameters
Moderator | Decoupled Water
Energy and Resolution | 10meV~1500 meV: 3%~10%
Flux | 10~1500meV: 4.98*107n/s/cm2@185kW
Beam size（sample） | MAX：5cm×5cm
Detector coverage | horizontal：-30˚～+60˚ vertical：-30˚～+30˚
Sample to moderator | 18m
Fermi to sample | 2m
Sample to detector | 2.5m
Sample environment | CCR（5K~800K） Superconducting magnet（～7T）
High energy inelastic spectrometer (BL05)

## Slide 25
Cold Neutron Inelastic Spectrometer (BL04)
The Cold Neutron Inelastic Spectrometer (CNIS) is designed to be a high resolution inelastic spectrometer, which will focus on efficiently detecting low energy signals such as magnetic excitations, phonons, and quasi-elastic signals using cold neutron.
25
Prof. Xing Tong
Dr. Yu Feng
Incident energy：1- 75 meV
Energy resolution: 2.5% (~1% at high resolution mode)
Combination of multiple choppers allows switching to high resolution mode freely and enables multiple incident energy modes
Schematic Diagram of Spectrometer Structure and Key Component Layout
Horizontal
Vertical
Guides are being manufactured at MirrorTron and planed to be installed in this summer. It uses 50 cm straight sections to approximate the curved and elliptical shape
Sample chamber is made of low magnetic permeability materials for magnets. The end guide can be switched to a strong-focusing guide and a polarization system
3He detector banks use an “ air box” solution
Vanes are installed between detector banks to prevent stray scattering
An oscillating radial collimator is installed in the sample chamber to prevent scattering from the sample environment

## Slide 26
beam
polarizer
sample
detector
analyzer
incident guide field
scattering
guide field
Preliminary Design： In the light of the low flux but sharp pulse width of the decoupled poisoned hydrogen moderator, PAINTER will incorporate the capabilities of both polarized inelastic neutron scattering and polarized neutron diffraction. The performance of beamline is optimized to a balanced point between a diffractometer and a spectrometer.
Moderator | Decoupled hydrogen
Best energy resolution | ΔE/E ≤ 5%
Neutron flux | ≥1×107 n/scm2
Neutron polarizability | ≥90% @5 meV
Polarizer | Polarized supermirrors
Analyzer | Wide-angle polarization 3He
Incident energy | 1 meV~80 meV
3 frame overlap disc choppers
2 high-speed disc choppers (pulse removal & monochromator)
Moderator-to-monochromator L1=23 m
Monochromator-to-sample L2=2.5 m
Sample-to-detector L3=2 m
Detector size: 8mm 3He tubes
Polarized neutrons: λ ≥ 2 Å (Ei ≤ 20 meV)
(Polarization scheme has not been fully finalized）
Direct Geometry Polarized Neutron Spectrometer (PAINTER, BL20)

## Slide 27: Indirect geometry Molecular Vibrational Spectrometer (BL06)
obtain molecular vibration spectra of materials
catalysts,
hydrogen storage materials
hydrogen bonded systems
hydrous minerals
MOF, zeolites,
biological samples such as drugs and biomolecules.
27
Time and energy double focused secondary spectrometer with large curved HOPG analyzer;
Large solid angle analyzer coverage, high flux, high energy resolution;
The neutron vibrational spectrum (NVS) and diffraction spectrum of the material are obtained simultaneously;
A variety of sample environments, such as dedicated closed-cycle refrigerator (CCR), high pressure, gas flow cells and gas manifold, in-situ Raman.
Large solid angle (≥4.5 sr) analyzer coverage, with a total of 14 modules
Dr. Chunyong He
Indirect geometry molecular vibration spectrometer (iMovies) is an inelastic neutron scattering instrument for neutron vibrational spectrum (NVS) . The optimum energy resolution (ΔE/E) is 1.5%.

## Slide 28: Progress of iMovies
Analyzer prototyping
Transmission test of Be filter
2024.4
Physical design review
2024.5-2025.9
2025.9
Construction and installation of chopper and guides
2025.10
2026.8
2027.4
2028.11
2029.7
scattering chamber installation
Commissioning
Day-one experiment
Open to users
2026.3-
2026.3-
Design and construction of Be filter
Analyzer tile assembly
Most of the major equipment will be completed for processing and installation by the end of this year.
28
iMovies 2026.4.10

## Slide 29: Neutron Backscattering Spectrometer (BL10)
Provide very fine energy resolution, <3.0µeV, good for probing dynamic processes in various systems on the ps-ns time scale.
29
V sample (3cm)，2.2μeV
bent silicon crystals for analyzer
Dr. Hongyu Guo

## Slide 30: Progress of NuBS
2024.01
Start CSNS II
2024.04
design
2024.10
construction
2025.07
Installation of 30m
2026.07
Accept of Hall
2027.03
Scattering chamber
2028.04
First neutron
g
2029.09
End CSNS II
2029.04
first experiment
2025.10
2025.10
2025.08
2025.08
2025.10
2025.07
2025.07
Instrument hall > 99%;
30 m finished;
Engineering design
Analyzer design finished
Physical design published
2025.05
2025.08
User meeting
Energy resolution < 3 μeV
30

## Slide 31
Outline
CSNS Instrument Suite
Powder & single crystal diffractometers
Large scale instruments
Inelastic spectrometers
Industry application and nuclear technique
Summary

## Slide 32
32
Engineering Material Diffractometer (BL08)
Built for Residual stress Analysis, Texture Analysis, Micromechanical behaviour of metals, Industrial metallurgy and manufacturing process simulation.
First beam： Dec.29 2022，Under commissioning.
Neutron wavelength 0.5-6.0Å
resolution  d/d ~ 0.25 %
Gauge volume 2, 3, 4, 6mm
sample table 1.8x1.8m, 2ton

## Slide 33
33
Atmosphere Neutron Irradiation (BL11)
The first neutron obtained April，2022
Good spectra shape with JEDEC
flux range:103-107 n/cm2/s (>10MeV)
Collimated beam (1-10cm) and extended beam (80cmx80cm)
Aim to neutron single event effect test for semiconductors, electronic devices and integrated equipment used in aviation and ground.
Thyristor Irradiation Experiment
Experiment of Board Level ICs
Notes: Neutron single event effect test for semiconductors, electronic devices and integrated equipment used in aviation and ground

## Slide 34
34
Energy resolved neutron imaging (BL13)
34
  Conventional neutron imaging
  Bragg edge imaging
  Grating imaging
  Neutron diffraction
  Spatial resolution 50 μm
  d/d ~ 0.5 %
  View field 200 x 200 mm2
First beam： Jan. 05 2023.
Adv. Funnct. Mat. 2024, 34, 2404495

## Slide 35
35
Industry Application Highlight
More than 8% beamtime for industry application

## Slide 36: Neutron Physics and application instrument (BL12)
NPAI ：Split-beam design, two beamlines;
Application Beamline : PGNAA and NDP
  PGNAA： Exchanger for beam size and background adjustment; Attenuator for flux adjustment;
  NDP：High rate mode by multiple detectors; NDP/NI system, 3D mapping mode by scanning sample;
  Physics Beamline: UCN
  UCN：Build China's first ultracold neutron source; A compact, SFHe4-based and high storage time UCN source .
Ultra Cold Neutrons（UCN）
NDP
PGNAA
NDP
UCN

## Slide 37: Neutron Physics and application instrument (BL12)
UCN Guide
Entire fabrication process development;
Surface roughness RMS: ~ 0.55 nm;
Density: ~ 93% bulk density.
PGNAA and NDP
The engineering design is in progress;
The production will be carried out in the second half of this year.
UCN convertor (CYTOP)
Spin coating on silicon wafer;
Thickness: 95.5 nm;
Optical potential: 111.4 neV;
Currently attempting: Dip coating.
UCN cryostat
A 0.5 K @ 100 mW ³He refrigerator cools ultrapure ;
⁴He to ≤ 0.7 K via a ³He/⁴He heat exchanger;
  Finalized cryostat process and design;
  Finished initial superleak tests (³He/⁴He ≈10-¹⁰).
Design and Progress of the Engineering
Finish the design of shielding, guide and chopper;
Shielding will be installed this year;
Guide and chopper will be installed next year;
The first neutron beam will be obtained in 2028.

## Slide 38: Neutron Technology Development Station （BL 08A）
Prof. Ping Wang
38
Test and development of neutron detectors, polarization, optics, single crystal orientation etc.
Support the construction and operation of the neutron instruments
Development of novel experimental methods using pulsed neutrons
Terminal 3 Device testing
Terminal 2
Neutron reflectivity measurement
Terminal 1
Orientation of single crystals
Design highlights
1. Versatile functions: three terminals
2. Lower background: Bender + T0 chopper
3. Higher beamtime utilization efficiency: automatic technology

## Slide 39: Neutron Technology Development Station （BL 08A）
2025.9.8
NTDS successfully achieved its first neutron beam on March 5, 2026
The neutron flux: 4.2*106 n/(cm2*s)
at 0.5 ~ 5.9 Å
Preliminary testing completed
1. Neutron beam characteristics
2. Chopper system performance
3. Detectors, DAQ, control, Data Analysis
4. Neutron reflectivity terminal commissioning

## Slide 40
40
The operation of CSNS goes well with high efficiency, eight Instruments fully open to users. three instruments under trial operation.
The CSNS-II instruments finished physical design. There are still many challenges of engineering design, key technology，manufacture, installation and commissioning.
Close collaboration with international colleagues are expected !
Summary

## Slide 41
Thank you ！